## Slide 1: Polarized Light Field Microscopy Using Deep Learning
3D birefringence measurements of transparent microscopic volumes
2022 Image Science Conference GRC. Emerging Imaging Techniques at the Intersection of Physics and Data Science, June 5 - 10, 2022
Grant Harris, Explorative.Engineering
Geneva Schlafly, University of Chicago
Dr. Rudolf Oldenbourg, MBL
Patrick La Viere, University of Chicago
Polarized Light Microscopy
Quantitative (magnitude + orientation) measurement of birefringent structures in living cells such as microtubules, actin, etc.,
Birefringence, diattenuation & fluorescence polarization for live cell imaging.
Calibration process to rectify geometry and intensity variations before iterative deconvolution for resolution recovery and aberration correction of 3D reconstruction.
Light Field Microscopy
microlens array
Recording and controlling the 4D light field in a microscope using microlens arrays. Levoy M, Zhang Z, McDowall I.J Microsc. 2009
Richardson-Lucy deconvolution
Acquisition of multiple polarizations (channels), using liquid crystal universal compensator
Polarized Light Field Microscopy
Measuring optical anisotropy of uniaxial, non-attenuating samples in 3 dimensions.
Forward Model: Optical Ray Tracing with Jones Calculus
Experimental
Simulated
Limited-Angle Tomographic Reconstruction of Birefringence:
Learning the Inverse Transform
Network Architecture: Incorporating Physics and Symmetries
Exploring how to incorporate known symmetries, group transforms into networks
Convolutional, 2D, 2.5D, 3D, …
Quaternion, Hyper/Complex-valued
Group Equivariant, Spherical, Steerable
Geometric Deep Learning
Graph Convolutional
Polarization Representations
Stokes, Mueller, Jones;
Geometric, Poincare sphere
Group SO(3)/SU(2),
Pauli Algebra,
Quaternion
(See Geneva Schlafly’s poster.)
Simulation confirmed with experiment
3D Birefringence
Γ: retardance
φ,θ: orientation
4D Light Field Image
microlens array
Γ, (φ,θ)
Convolutional neural network
Rays hitting sensor behind
single lenslet
Optical System
Object Volume
Jones vector/ matrix interaction
We use geometric ray-tracing with optical elements as a series of birefringent voxels, with intersection lengths calculated with the Siddon algorithm.
The process is noncommutative.
Explorative.Engineering
Architectural Dynamics of Living Cells Laboratory established by Dr. Shinya Inoue. Dr. Oldenbourg invented the LC-PolScope in 1999. The focus is on the development of instrumentation in collaboration with biological investigators
Vari-LC polarization state controller utilizing liquid crystal variable retarders.
Devices and software available from OpenPolScope.org
4D light field acquisition using plenoptic camara
We are developing a napari plug-in for Light Field Microscopy Imaging
for LFM Reconstruction with iterative and deep learning approaches.
Birefringent
element
[Γ, (φ,θ)]
[Γ, (φ,θ)]
Physics-informed,
train with synthetic data
using forward model
Exploiting Inherent Bias
Deep Priors
Generative adverserial
Variational autoencoders